## Slide 1: Evaluating a Process Change for Effectiveness, Safety, Waste Generation, & Air Emissions Reduction. CASE STUDY: Improving Dip Room Cleaning Protocol
Kale Walch, Hexcel and Mike Sherer, Trinity Consultants

## Slide 2: Facility Description
Manufacturing of honeycomb blocks
  On site since 1966
  Dip Room
  RTOs for control of VOCs
CAA permits
  PSD construction permit requiring BACT controls
  Title V operating permit
RCRA
  Large Quantity Generato

## Slide 3: Honeycomb

## Slide 4: Historic Process
Acetone used for floor cleaning
No removal of liquid / resin material
Disadvantages
  Resin build up
  Lower Explosive Limit (LEL) sensors registered high during cleaning
    Sensors are actually measuring Lower Flammable Limit (LFL)
Advantages
  No waste generated
  Acetone evaporated quickly
  Smoothed out floor

## Slide 5: Project Scope
Project team
  Operators, EH&S Staff, Consultant
Find a new chemical
  Tested alternative did not work
Changed to process improvement
  Kept acetone as the cleaning solvent
  Still completed at shift change

## Slide 6: Changes
100% acetone replaced with 70% water / 30% acetone
Implementation Problems
  Had to ground bucket
  Had to purchase a ringer
  Floor changed color and became bumpy
  Created a hazardous waste
    Added a satellite drum for collection
  Moved to purchase of pre-diluted mix
    Purchased hand pump to dispense

## Slide 7: Dip Room

## Slide 8: Changes (continued)
Implementation Successes
  Identified and resolved historic safety risks
    Grounding
    LEL sensor impact reduced
  Floor became cleaner and cleaner
    Resolved roughness issue over time

## Slide 9: Cleaning Product and Waste

## Slide 10: Changes (continued)
Implementation benefits
  Estimated acetone emission reduction of 12 tpy
    Acetone is not a regulated air pollutant, thus not reflected in the annual emission inventory
  Chemical use cost reduction of $32,000 per year (based on 50 week a year)
  Recently complemented on dip room cleaning during ISO audit
  Utilized to clean other areas
Implementation disadvantages
  Hazardous waste disposal cost
  Some areas, i.e. tank edges, still need cleaning with 100% acetone

## Slide 11: Lesson Learned
Had to convince long time employees change is possible
Involved operators in scoping, design and implementation
Changes made during implementation required
Results improved over time