## Slide 1: Air Quality Permitting Guidelines for Industrial Sources
Pinal County Air Quality Workshop
Florence – February 15, 2018
Anu Jain – Air Quality Engineer

## Slide 2: Who needs an industrial permit?
Facilities that have a potential to emit 5.5 pounds per day or 1 ton per year of any regulated pollutant.

## Slide 3: Regulated Pollutants
Nitrogen Oxides (NOx)
Carbon Monoxide (CO)
Sulfur Dioxide (SO2):
Volatile Organic Compounds (VOCs)
Hazardous Air Pollutants (HAPs)
Particulate Matter (PM10/PM2.5)

## Slide 4: What is the purpose of a Permit?
-Identifies air quality rules that a source is subject to: Local (PCAQCD), State (Statutes) or Federal (EPA).
-Contains emission limits for each significant emission unit.
-Defines allowable hourly, monthly or annual throughputs.
-Monitoring, recordkeeping, and reporting requirements.
-May contain limitations to avoid stringent air quality requirements or higher fees.

## Slide 5: Types of Permits
Class I
-New Source Review sources (PSD or NNSR)
-Title V sources (above “major source” thresholds)
Class II
-Synthetic minor sources
-Medium & small spray paint operations, feed mills, metal fabrication crushing/screening, cotton gins, crematories etc.
Class III
Small gas stations, auto body shops, dry cleaners…

## Slide 7: Stationary Sources and PM Nonattainment
Small sources
  Area source rules may be incorporated into permits
Medium sources
  Area source rules may be incorporated into permits
  Source might have to take Federally Enforceable limits to stay under 100 tons per year (tpy)
  May have to implement Reasonably Available Control Technology (RACT) level controls
Large sources
  Area source rules may be incorporated into permits
  Nonattainment New Source Review (NNSR) for sources with a PM10 potential to emit (PTE) over 100 tpy
  New sources must install Lowest Achievable Emission Rate Technology (LAER) which does not consider economic impacts
  Existing sources must implement Reasonably Available Control Technology (RACT) level controls
  Offsets at a ratio of at least 1:1 will be required

## Slide 8: New Permit
-Permit Application
-Additional Forms (if applicable) for Fuel Burning equipment, Storage Tanks, Crushing and Screening equipment, Cotton Gins, Generators, Soil Vapor Extraction Units, Spray Paint Booths and Wastewater Treatment Plants.
- Generic Outline or Air Quality Permit Filing Instructions (process description, site plan, flow diagram, plant and equipment capacities, MSDS sheets etc.)
-Application fee
Forms available at http://www.pinalcountyaz.gov/Departments/AirQuality/Pages/IndustrialPermits.aspx

## Slide 9: New Source Performance Standards NSPS (40 CFR Part 60)
Db – Industrial-Commercial-Institutional Steam Generating Units
GG – Stationary Gas turbines
LL – Metallic Mineral Processing Plants
OOO – Nonmetallic Mineral Processing Plants
UUU – Calciners and Dryers in Mineral Industries
IIII – Compression Ignition Internal Combustion Engines
JJJJ – Spark Ignition Internal Combustion Engines
KKKK – Stationary Combustion Turbines

## Slide 10: Area Source NESHAPs (40 CFR Part 63)
6H’s – Paint Stripping and Miscellaneous Surface Coating ( includes Autobody shops)
6W’s – Plating/Polishing
6X’s – Metal Fabrication/Finishing
6Z’s – Aluminum, Copper and other non-ferrous Foundries
7C’s – Paint Manufacturers
7D’s – Prepared Feed Manufacturers.
4Z’s (RICE) – Diesel and Natural Gas Engines.
6H’s – Paint Stripping and Miscellaneous Surface Coating ( includes Autobody shops)
6W’s – Plating/Polishing
6X’s – Metal Fabrication/Finishing
6Z’s – Aluminum, Copper and other non-ferrous Foundries
7C’s – Paint Manufacturers
7D’s – Prepared Feed Manufacturers.
4Z’s (RICE) – Diesel and Natural Gas Engines.
-Each one contains a specific Compliance Date.
-Must submit INITIAL NOTIFICATION.
-Brochures available at
www.epa.gov/ttn/atw/area/arearules.html

## Slide 11: Fees
-Application Fee (Non-refundable)
-Permit Processing Fee (not applicable to Class III sources or transfers)
-Annual Fee
-Emissions Fee (only for Class I sources)
*Fees for 2018 is posted on our website.
*Fees are adjusted annually by the Consumer Price Index (CPI).

## Slide 12: Renewals
Permits valid for 5 years.
Letters to renew permits are mailed at least couple of months before the permit expiration date.
Revisions/Transfers do not start the
clock.

## Slide 13: Permit Changes
TYPES:
-Permit Revision: Changes in equipment, process, and or products.
-Permit Transfer: Ownership or facility name change

## Slide 14: Permit Revision Application
-Same application form as for “New” permits, but check “Revision” box.
-Same information needed as for “New” permits, but only in relation to changes and or modifications.
-Revision application fee applicable to Class I permits only.

## Slide 15: Permit Transfers
-Same Application form but check “Transfer” box.
-Apply before the transfer occurs.
-No processing fee associated with transfers.
-Transfers cannot be used for location changes, a new permit must be issued.

## Slide 16: Permit Issuance Timeframes
-Mandatory Public Notice period of 30 days for new permits, significant revisions, and renewals.
-Class I permits have an additional mandatory EPA review period of 45 days.
-Permit processing time depends on the complexity, and the completeness of the application.

## Slide 17: Issues
Some of the issues related to permitting:
-Operating without a permit.
-Adding an emission unit without revising the permit.
-Process or equipment list not getting updated during renewal.
-Permit transfer.
-Not reading the permit.
-Not asking questions.

## Slide 18: Who to call?
Anu Jain
Air Quality Engineer
(520) 866-6931
anu.jain@pinalcountyaz.gov