## Slide 1: Environmental Compliance Assistance for Business & Industry Energy Conservation
Steven Kessler
  Director, aero Facilities & Maintenance for the Americas

## Slide 2: Steven Kessler Director, Facilities & Maintenance for the Americas
Background: Adjunct Professor – PVCC (Business Concentration)
School: Purdue University – BS: Industrial Engineering Technology, Keller Graduate School of Management – MBA: Information Systems Management/Healthcare, Grand Canyon University – Doctorate: Business Administration/Management (2/2020)
Certifications: RCGC – AGA/IGT
Previous Experience: Logistics/Shipping, ESCO, Controls, Construction, Dual Fuel Investor Utility
Years with HON: 9 Months

## Slide 3: Goals & Objectives
How critical is sustainability?
Understanding Common Terms.
Quick Reference Notes.
What can we all do to save energy.
What is PF (Power Factor).
What Honeywell has accomplished – We're not done yet.
Smart Buildings

## Slide 4: Sustainability – Definition
“Sustainable development is
development that meets the
needs of the present without
compromising the ability
of future generations to
meet their own needs.”
Brundtland World Commission on
Environment and Development definition
An Objective Without a Plan is Just a Wish

## Slide 5: Biggest Concerns
93% - Climate Change
91% - Education
83% - Income Equality
82% - Immigration
75% - Reproductive Rights
69% - Trade
Fast Company – Nov. 2019
People Surveyed with Greatest Concerns/Impacts

## Slide 6: Key Concepts
BTU: One British Thermal Unit (BTU) represents the amount of heat that is required to raise or lower the temperature of 1 pound of water by 1 degree Fahrenheit. Most air conditioners are measured using BTUs.
BTUh: Some systems measure their energy by British Thermal Units per Hour (BTUh). The energy that is extracted from your home by an air conditioner is measured in BTUs, while the cooling and heating capacities are referred to in BTUh. For reference, 12,000 BTUh is equal to 1 ton of cooling.
EER: Energy Efficiency Ratio (EER) of a cooling unit is determined by the output cooling divided by the electrical power input. As opposed to Seasonal Energy Efficiency Ratio (SEER), which is calculated over a range of outside temperatures, EER is typically determined by a set outside air temperature, a set inside air temperature and 50 percent relative humidity. For reference, 11 EER is roughly 12 SEER.
Level setting with key terms

## Slide 7: Key Concepts
HSPF: The Heating Seasonal Performance Factor (HSPF) is used to measure the efficiency of a heat pump. The HSPF is a ratio of the heat output to electricity use over an average heating season. The higher the HSPF, the greater the energy efficiency.
SEER: Seasonal Energy Efficiency Ratio (SEER) measures air conditioning and heat pump cooling efficiency, which is calculated by the cooling output for a typical cooling season divided by the total electrical energy input during the same time frame. The higher the SEER rating, the greater the energy efficiency, and, in turn, the lower your energy cost.
Level setting with key terms

## Slide 8: Key Concepts - HVAC
Air Movement 6 ACH or 1 CFM/ft2
Ventilation Rate 5 CFM/person
Lighting T12s: 1.2 W/SQFT, T8s: 0.8 W/SQFT
LEDs: 0.4 W/SQFT
LEDs use 50% of CFLs
Chiller Size 300-600 ft2/ton, Ton 12,000 BTU/ton
People Load 450 BTU/person/hr.
People Density Office 140 ft2/person
Theater 14 ft2/person
Level setting with key terms

## Slide 9: Key Concepts – Lighting
Level setting with key terms

## Slide 10: Power Factor – Simplified
Understanding PF%

## Slide 11: Power Factor – Simplified
Understanding PF%
Poor power factor means that you’re using power inefficiently. This matters to companies because it can result in:
Heat damage to insulation and other circuit components
Reduction in the amount of available useful power
A required increase in conductor and equipment sizes
Finally, power factor increases the overall cost of a power distribution system because the lower power factor requires a higher current to supply the loads.

## Slide 12: Executive summary
  Honeywell AERO operates 11 major office/engineering and manufacturing sites in Arizona
  From 2016 to 2018 Honeywell AERO sites in Arizona completed 431 energy and water saving projects
    Carbon savings of 26,517,937 lbs. per year
    Energy savings of 87,152,712 Kbtu per year
    Water savings of 9,903,839 gallons per year
    Costs savings of $2.56M per year
    Investment of $ 6.52M

## Slide 13: Lighting projects
240 projects – convert HID and fluorescent lighting to LED including building exterior, offices lighting and production area lighting
  14,672,881 kbtu energy savings
  Top Sites and Projects
    Glendale – 27 LED retrofit projects
    Sky Harbor – 10 LED retrofit projects
    Phoenix – 91 LED retrofit projects
    Tempe – 24 LED retrofit projects
    Deer Valley – 26 LED retrofit projects
    Tucson – 36 LED retrofit projects

## Slide 14: Cooling plant/systems projects
12 projects
  20,917,991 kbtu energy savings
  Top Sites and Projects
    Deer Valley – Replacement of 2 Central Plant chillers
    Phoenix – Replacement of 1 Central Plant chiller
    Sky Harbor – Replacement of 3 Central Plant chillers
    Tucson – Replacement of 3 Central Plant cooling towers
    Phoenix – Replacement of 6 Evaporative coolers

## Slide 15: Compressed air projects
23 projects
  23,273,529 kbtu energy savings
  Top Projects
    9 sites conduct ultrasonic compressed air leak surveys – 21 surveys completed
    Deer Valley – replace fixed speed air compressor with variable speed drive air compressor

## Slide 16: Water savings projects
29 projects
  9,903,839 gallons water savings
  Top Projects
    Tucson - Install make-up water conductivity meters on cooling towers
    Tempe – Install new dishwasher and water saving restroom fixtures
    Phoenix – Xeriscaping and water saving restroom fixtures
    Sky Harbor – Xeriscaping and water saving restroom fixtures

## Slide 17: HVAC and control systems projects
59 projects including installation of programmable thermostats, building automation system enhancements, variable speed drives on air handling units, high efficiency boilers, high efficiency motors, economiser control programs, chiller optimization control system, and setpoint/schedule optimization
  20,743,389 kbtu energy savings
  Top Projects
    Tucson - Replace boilers with high efficiency boilers
    Tempe – Building Automation System program and controls upgrades
    Phoenix – Setpoint/Schedule optimization, programmable thermostats
    Sky Harbor – Install central plant chilled water optimization system
    Deer Valley – Variable speed drives on cooling towers

## Slide 18: Smart Building Solutions
Enterprise Buildings Integrator (EBI)

## Slide 19: THANK YOU
        Contact information
        Email: Steven.Kessler@Honeywell.com
        Phone: 602.245.4080
We Shape the Future of a Smarter, Safer, and more Sustainable World
HSEF: Safe & Sustainable
Questions?
Notes: Closing slide