## Slide 1: Arizona Department of Environmental Quality Mulit-Sector General Permit (2019)
Christopher Henninger, Supervisor
Surface Water Permit Unit

## Slide 2
Today’s Agenda:
What is the “MSGP”
Legal / program updates
Changes to 2019 permit
myDEQ
Schedule

## Slide 3
The Clean Water Act (Section 402)
establishes the:
National
Pollutant
Discharge
Elimination
System
In Arizona, we call it AZPDES

## Slide 4
Early NPDES permits focused primarily on Wastewater Treatment Plants
CWA was amended in 1987 to include stormwater:
Municipal
Construction
Industrial

## Slide 5
Construction
MS4
Industrial
NPDES Stormwater Program Regulates

## Slide 6
Facilities Subject to Standards
Heavy Manufacturing
Mining / Oil and Gas
Hazardous Waste Facilities
Landfills
Recycling Facilites
Steam Electric Power Plants
Transportation Industries
Sewage Treatment Plants
Large Construction
Light Industry
Industrial Stormwater Covers 11 Categories

## Slide 7
The 11 categories are further broken down by
Sector
Subsector, and
Standard Industrial Classification (SIC) Code.

## Slide 8
2010 Permit
All permittees had to prepare and annual report
Some permittees had to submit the annual report to ADEQ
2019 Permit
No Annual Report requirement
Prepare and submit a Control Measure Assessment Report (CMAR) when an Action Level is exceeded (Part
Prepare and submit a Corrective Action Report (CAR), when a corrective action triggered (Part
Reporting

## Slide 9
2010 Permit
Benchmark monitoring 4X’s/yr with potential to discontinue
Averaging sample results
Benchmark concentrations set at U.S. EPA Water Quality Criteria
Included various analytical parameters that do not have a standard
2019 Permit
Routine Analytical Monitoring 2x’s/yr for duration of permit coverage
Report discrete results
Incorporates Arizona Surface Water Quality Standards (SWQS) as Action Levels
Added, removed, or substituted various parameters
Applies SWQS for designated use of the receiving water
Analytical Monitoring

## Slide 10
2010 Permit
Report monitoring results within 3 months of end of monitoring period (up to 15 months from when the sample was collected
Use hardness table for hardness dependent metals
2019 Permit
Submit eDMR within 30 days of receiving results
Enter hardness value (eDMR will automatically calculate concentration for hardness dependent metals)
Discharge Monitoring Report

## Slide 11
2010 Permit
32 business days for ADEQ review (40 +/- days)
Submit SWPPP for sites within 2.5 miles of impaired water or Outstand Arizona Water, regardless of pollutant
2019 Permit
Reduced to 30 calendar days for ADEQ review (review most often completed within 7 days)
Using myDEQ, filter impairments and industrial activities to reduce SWPPP submissions when the facility is unlikely to contribute additional pollutant loading for the impaired water
Stormwater Pollution Prevention Plan

## Slide 12
MSGP 2019 Implementation Schedule
Issued May, 2019
Becomes effective January 1, 2020
Existing permittees must submit a Notice of Intent (NOI) to obtain coverage under MSGP 2019 between:
January 1, 2020 and February 28, 2020

## Slide 13
NOI Must be Submitted Electronically Using myDEQ
Establish myDEQ account if not already completed
Complete each screen with complete and accurate information
Authorization is issued upon completing the NOI path (including the fee component)

## Slide 14
Benefits of E-Notice of Intent (NOI):
Completeness (mandatory fields)
Business rules to lead customer to permitting requirements (poka-yoke)
Built in tools for more accurate information

## Slide 15
Mapping Tool to Assist Customers with
Accurately Locating their Site

## Slide 16
Example from Industrial Stormwater Permitting Path to Identify Sector(s)

## Slide 17
Interactive Mapping Tool to Assist with
Identifying Outfall Location(s)

## Slide 18
Outfall Summary Table

## Slide 19
Monitoring Requirements Generated
Based on Customer Input

## Slide 20
Customer’s Dashboard to Manage Permit Actions

## Slide 21
Questions
Contact
Christopher M. Henninger, Supervisor
Surface Water Permits Unit
Arizona Department of Environmental Quality
602-771-4508
Henninger.Christopher@azdeq.gov

## Slide 22: Table Slide
Title 1 | Title 2 | Title 3 |  | Title 4 |  | Title 5
 |  | Subtitle 1 | Subtitle 2 | Subtitle 3 | Subtitle 4 | 
Content 1a |  |  |  |  |  | 
Content 1b |  |  |  |  |  | 
Content 1c |  |  |  |  |  | 
Content 1d |  |  |  |  |  | 
Content 1e |  |  |  |  |  | 
Content 1f |  |  |  |  |  | 
Content 1g |  |  |  |  |  | 
Content 1h |  |  |  |  |  |