## Slide 1
Type of vehicle/equipment
  Best candidates for MERC projects are usually heavy-duty diesel vehicles and engines
  Diesels have higher NOx and PM emissions
  Heavy-duty vehicles/engines tend to have high operating rates
  Light-duty vehicles tend to have low emissions and lower usage rates
Availability of data on candidate and replacement vehicles
  Model-year, engine family, annual operating hours/miles, load factors
Cost of the project
  Price and operating costs of replacement vehicles/engines
  Loss in value of vehicles being replaced
Factors to Consider in Evaluating MERC Projects

## Slide 2
Emissions are estimated for current and replacement vehicle using U.S. EPA’s MOVES3 model
  MOVES3 is U.S. EPA’s official model for estimating mobile source emissions
  Can provide emission rates by model-year, vehicle category, vehicle/equipment type, and fuel type
  Accounts for emission control system deterioration
  Includes default values for vehicle operation and load factors which can be used or replaced with actual values
  Can account for local conditions such as traffic speeds and ambinet temperatures.
Quantification of MERCs

## Slide 3
Substitute new 10 electric transit buses for 10 new diesel buses
  MERC Values: NOx = 1.00 tpy, PM = 0.0016 tpy
Replace existing one 175 - 600 horsepower Tier 2 diesel engine/equipment with a Tier 4 final engine
  MERC Values: NOx = 0.32 tpy, PM = 0.018 tpy
Replace 1,000 new gasoline passenger cars with zero-emission vehicles
  MERC Values: NOx = 0.20 tpy, PM = 0.020 tpy
Replace 1,000 new full-size gasoline pickups with zero-emission vehicles
  MERC Values: NOx = 0.55 tpy, PM = 0.076 tpy
Quick MERC Examples