## Slide 1: Arizona Environmental Strategic Alliance May 16, 2023
Pinal County Air Quality Control
Scott DiBiase, Interim Director

## Slide 2
West Pinal Serious PM10 Nonattainment Area
Source: 2022 Serious Area Particulate Plan for PM-10 For The West Pinal County Nonattainment Area, May 2022. Maricopa Association of Governments [MAG SIP]

## Slide 3: West Pinal State Implementation Plan (SIP)
2020 - West Pinal redesignated to Serious PM10 NAA (attainment by end of 2022)
MAG Serious Area “Commitments” SIP submitted to EPA May 2022
    Pinal County BOS Adopted more stringent construction/general fugitive dust rules in January, go into effect June 1st.
    EPA has approvability issues with submitted SIP
2/15/23 - EPA Proposed Finding of Failure to Attain (by 12/31/22)
MAG 5% plan due to EPA by end of 2023
Chart: PM10 Exceedance Days (2020-2022)
| Hidden Valley | Stanfield | Maricopa | Eloy | Eleven Mile Corner | Casa Grande | Combs
PM10 Exceedance Days | 95 | 10 | 6 | 5 | 4 | 3 | 1
PM10 Standard | 3 | 3 | 3 | 3 | 3 | 3 | 3

## Slide 4: West Pinal PM10 Nonattainment Area New Requirements
Construction
  Dust Control Plan – control measures* to be implemented at all times
    *Primary and contingency control measures
    Minimum water onsite requirements
  Basic dust control training/certification – water truck/pull drivers, site super (1+ acres)
  Comprehensive dust control training/certification – Dust Control Coordinator (DCC)
    5 acres and larger of ground disturbance worksites
  Daily site inspections and recordkeeping
  Register for West Pinal dust control forecast - https://public.govdelivery.com/accounts/AZDEQ/subscriber/new
  Stabilization and opacity standards
    Includes property line (no visible emissions exceeding 30 seconds in any 6-minute period)
  Trackout – clean up immediately when extends 25+ feet
Rules located online at https://www.pinal.gov/415/Pinal-County-Code-of-Regulations

## Slide 5: New West Pinal “Training”/Certifications
Basic/Comprehensive Dust Control certification quizzes are online
  https://www.pinal.gov/331/West-Pinal-Nonattainment-Area
No formal training course – referred to rules and can take “open book” quiz

## Slide 6
West Pinal PM10 Nonattainment Area Requirements
General fugitive dust
  Unpaved roads, open areas/vacant lots (including vehicle use), unpaved parking lots, paved roads, etc.
    Requirements:
    Unpaved roads – 26+ ADT threshold for visibility and stabilization requirements
    Annual road paving – Starting in 2024 – responsible entities (County, cities, state) are to
      Pave an avg. of 20% of their unpaved roads annually, up to a max. of 5 cumulative miles
      Contingency measure – speed limit on unpaved roads (26 ADT) – 15 mph
    Annual unpaved roads reporting
    Trackout – clean up immediately when extends 25 feet or more
    Paved roads street sweeping –In 2025 requirement to use only certified street sweepers
    Rules located online at https://www.pinal.gov/415/Pinal-County-Code-of-Regulations

## Slide 7: Ozone Nonattainment Area
2015 Ozone NAAQS -70 ppb
    MAG Moderate nonattainment area SIP – TBD
      Suggested list of control measures
      Board rulemaking commitment - TBD
      Ozone RACT/RACM rulemaking - TBD
    Redesignation to Serious nonattainment?
      Offsets rulemaking(s)?
  Ozone NAAQS reconsideration (CASAC initial thoughts - 55-65 ppb)
    Larger portion of Pinal County in Nonattainment?

## Slide 8: Pinal County Air Quality Permitting
Economic growth continues
    LG
    Lucid
    Kohler
    Proctor & Gamble
  In 2022 Department issued
    1,800+ dust permits (approx. ¾ in West Pinal)
    Nearly 1,800 open burning permits

## Slide 9: Thank you
Scott DiBiase
Scott.dibiase@pinal.gov
(520)866-6969
https://www.pinal.gov/305/Air-Quality